## Slide 1: Is the Hardware Z-Buffer Doomed?
lecturer: Eric Haines, erich@acm.org

## Slide 2: Why Hardware?
“The advantage of hardware rendering over software is limited to a single reason - speed.”
  - Steve Hollasch, Microsoft Fahrenheit designer

## Slide 3: Why Z-Buffer?
“… the brute-force approach … is ridiculously expensive.”
- Sutherland, Sproull, and Schumacker, A Characterization of Ten Hidden-Surface Algorithms, 1974

## Slide 4: Strengths of the Z-Buffer
Simplicity
Fixed memory costs
Clean mapping of data to screen (xform, cull, clip, interp)
Input data order is (usually) unimportant

## Slide 5: Z-Buffer Hardware, Jan. 2000
NVIDIA GeForce256 for the PC, 15 million polygons/sec, 480 megapixels/sec fill rate, hardware transform and lighting
Sony Playstation2 game console, to be released 3/4/00, 20 million polygons/sec, 1.2+ gigapixels/sec

## Slide 6: Trends
Moore’s Law:1.7x increase in CPU speed per year
Graphics accelerators are 2x to 4x, (Poulton gives 2.4x since 1986)
Gates on a graphics accelerator > gates on an Intel processor

## Slide 7: By the year 2010 (not)
Moore’s Law gives 10x every 5 years, so CPUs are 100x faster in 2010.
GA speedup
10 years
vs. CPU
2x
1,000x
10x
2.4x
6,000x
60x
3x
59,000x
590x
4x
1,000,000x
10,000x

## Slide 8: Z-Buffer Shading
Gouraud interpolation
Multipass
Multitexture
Heidrich, SGI Clearcoat BRDF work:
Arbitrarily complex local shading models will be possible.

## Slide 9: Possible Z-Buffer Weaknesses
Transparency
Antialiasing
Sampling
Filtering
Primitives
Bandwidth
Linear Performance
Reshading
Parallelization
Global Effects
Shoehorning

## Slide 10: Weakness: Transparency
Two basic algorithms :
Screen door
Back to front alpha compositing

## Slide 11: Screen-Door Transparency
Apply a checkerboard pattern.
Order independent
But:
Limited to one transparent surface
Limited to alpha of 0.5
Quality is low

## Slide 12: Screen Door Limitations

## Slide 13: Alpha Transparency
Must be done in back to front order.
This implies sorting. Either:
Host must send data in proper order.
- or -
Transparent surfaces must be stored and sorted on the accelerator.

## Slide 14: Weakness: Antialiasing
Good polygon edge antialiasing is costly. Approaches include:
Supersampling
Accumulation Buffer
T-Buffer
Multisampling/A-Buffer

## Slide 15: Supersampling
Simple idea: render at a high resolution, filter down.
Memory intensive, and sampling is fixed to a grid.
Exists now, but is slow; still, a possible future.

## Slide 16: Accumulation Buffer
Render the scene a number of times and blend results.
Trades less memory for more time compared to supersampling.
Higher quality shading vs. A-Buffer, and fixed memory.
Depth of field and motion blur.

## Slide 17: T-Buffer
Essentially a parallel Accumulation Buffer (but parallel only for antialiasing), by 3dfx.
Needs no extra programming.
Expensive in memory and processors.

## Slide 18: T-Buffer example

## Slide 19: Multisampling Fragments
0 0 0 0
0 0 0 0
0 1 1 0
1 1 1 0
0 0 0 0
1 1 0 0
1 0 0 0
0 0 0 0
1 1 1 1
1 1 1 1
1 1 1 1
1 1 1 1

## Slide 20: Multisampling Characteristics
Multiple fragments must be stored per pixel - more memory.
Also solves transparency problem.
Closely related to Z-Buffer.
Used in flight simulator community, high-end machines.

## Slide 21: Weakness: Sampling
Regular sampling gives aliasing.
Accumulation buffer can help, but sampling is still regular.

## Slide 22: Weakness: Filtering
“A pixel is not a little square” x 3
  - Alvy Ray Smith
Z-buffer filtering:
Extent is always one pixel cell.
Kernel is almost always box filter.

## Slide 23: Texture Filtering
Strongly supported by Z-Buffer hardware (e.g. anisotropic filtering).

## Slide 24: Weakness: Primitives
Limits of using only triangles:
Data explosion (in storage & bus) for curved surfaces.
  Partial solution is API support for Beziers & subdivision surfaces.

## Slide 25: Primitives (continued)
Image-based, volumetric, hypertexture, non-photorealistic, and other schemes have to be converted to triangles.
  Partial solution is using textures and variable alpha blending.

## Slide 26: Weakness: Bandwidth
Host Accelerator architecture; the bus between the two is a bottleneck.
  New primitives can help
  Geometric compression can help
At what point is it cheaper to send pixels instead of polygons?

## Slide 27: Bandwidth Analysis
Polygonal mesh: each vertex shared by 6 triangles.
Each vertex has a position, normal, and one texture coordinate pair (at least).
Triangle loop itself needs 3 bytes (for a mesh with <= 256 vertices)

## Slide 28: Bandwidth Analysis (cont.)
Triangle takes:
3*(3 XYZ floats + 3 normal floats + 2 UV floats) / 6 + 3 bytes for each loop =
19 bytes per triangle
There are 3 bytes per pixel (RGB)
So a triangle must be visible at 19/3 ~= 6 pixels to cost less than sending the pixels.
(idea by Steve Hollasch)

## Slide 29: Weakness?: Linear Performance
Common wisdom:
Ray tracing O(log n) vs. Z-buffer’s O(n).
Z-buffer efficiency schemes include:
hierarchical frustum culling
cell & portal
occlusion checking (HOM, HP Visual fx)
hierarchical Z-Buffering

## Slide 30: Weakness?: Reshading
Common wisdom: Z-buffer reshades each pixel many times. Rising depth complexity and shading costs will slow the Z-buffer.
(Pixar spends 60+% time shading)

## Slide 31: Reshading Mean Cost
The equation is (Cox & Hanrahan, 1993):
shadings(n) = 1 + 1/2 + 1/3 + … + 1/n
~= log(n) + 0.577
Depth Complexity
Shadings
4
2.08
11
3.02
31
4.03

## Slide 32: Weakness: Parallelization
“The enemy of parallelism is coherence” - Jim Kajiya
Parallel rendering as a sorting problem (Molnar/Cox/Ellsworth/Fuchs, 1994)

## Slide 33: Alternate Architectures
PowerVR (Dreamcast) tiling architecture
PixelFusion, based on PixelPlanes
Flight simulators

## Slide 34: Weakness: Global Effects
Limited to various hacks or preprocesses:
shadows
reflection
refraction
radiosity related

## Slide 35: Z-Buffer Global Illumination
Jason L. Mitchell

## Slide 36: Z-Buffer Global Illumination
Jim Arvo
Paul Diefenbach

## Slide 37: The Obvious Answer
Ray tracing: global, embarrassingly parallel.
But:
Usually needs shared memory or a copy of the database at each node.
Currently can be done, but for static scenes; efficiency scheme is a preprocess.
Is Pixar’s ray server a possible hybrid future?

## Slide 38: Single Processor Sphereflake
10 seconds a frame today,
10 frames/second by 2010

## Slide 39: Weakness?: Algorithm Shoehorning
“Special-purpose processors always choke off real algorithmic creativity”
- Jim Blinn

## Slide 40: Wheel of Reincarnation
Coined by Myer and Sutherland, 1968.
The wheel turns: GeForce256 GPU, ATI SOC
CPU only
CPU & GA
CPU & GPU

## Slide 41: Buffers
A-buffer - Carpenter, 1984
G-buffer - Saito & Takahashi, 1991
M-buffer - Schneider & Rossignac, 1995
P-buffer - Yuan & Sun, 1997
T-buffer - Hsiung, Thibadeau & Wu, 1990
W-buffer - 3dfx, 1996?
Z-buffer - Catmull, 1973 (?)
ZZ-buffer - Salesin & Stolfi, 1989
Accumulation Buffer - Haeberli & Akeley, 1990
Area Sampling Buffer - Sung, 1992
Back Buffer - Baum, Cohen, Wallace & Greenberg, 1986
Close Objects Buffer - Telea & van Overveld, 1997
Color Buffer
Compositing Buffer - Lau & Wiseman, 1994
Cross Scan Buffer - Tanaka & Takahashi, 1994
Delta Z Buffer - Yamamoto, 1991
Depth Buffer - 1984
Depth-Interval Buffer - Rossignac & Wu, 1989
Double Buffer - 1993
Escape Buffer - Hepting & Hart, 1995
Frame Buffer - Kajiya, Sutherland & Cheadle, 1975
Hierarchical Z-Buffer - Greene, 1993
Item Buffer - Weghorst, Hooper & Greenberg, 1984
Light Buffer - Haines & Greenberg, 1986
Mesh Buffer - Deering, 1995
Normal Buffer - Curington, 1985
Picture Buffer - Ollis & Borgwardt, 1988
Pixel Buffer - Peachey, 1987
Ray Distribution Buffer - Shinya, 1994
Ray-Z-Buffer - Lamparter, Muller & Winckler, 1990
Refreshing Buffer - Basil, 1977
Sample Buffer - Ke & Change, 1993
Shadow Buffer - GIMP, 1999
Sheet Buffer - Mueller & Crawfis, 1998
Stencil Buffer - 1997?
Super Buffer - Gharachorloo & Pottle, 1985
Super-Plane Buffer - Zhou & Peng, 1992
Triple Buffer
Video Buffer - Scherson & Punte, 1987
Volume Buffer - Sramek & Kaufman, 1999

## Slide 42: References
http://www.realtimerendering.com/doomed/